## Slide 1: COLD WEATHER TESTING AT CESSNA
Notes: Began this project as a simple presentation to the Flight Test Safety Symposium
However, as I investigated our methods of cold weather testing, I kept stumbling upon more and more information that needs to be shared.

## Slide 2
The secret of a good sermon is to have a good beginning and a good ending; and to have the two as close together as possible -- George Burns
Notes: This is a great theory. But, it is difficult to stick to the George Burns school of sermon-ology.

## Slide 3: COLD WEATHER OUTLINE
Why do we test in cold weather
What regulations are applicable
How do we coordinate in natural conditions
How do we coordinate in the lab
Summary
Notes: After investigating the current regulations/requirements, we had to differentiate between laboratory, and natural conditions.

## Slide 4: Why
Thought I would ask three of our senior members of the Cessna team
Notes: When I was learning the ins and outs of flight testing at McDonnell Douglas, I quickly learned to approach grey beards. You know. The old timers.
So, I chose these three, and asked them for their inputs on cold weather testing.

## Slide 5: Why, (First Senior)
He smiled and said that’s a great story.
Notes: This gentleman is a graduate of the Air Force test pilot school, retired officer, retired FAA, retired McDonnell Douglas, and working on his next retirement at Cessna
Apparently, the first applicant for cold weather certification went to the FAA and asked why any testing was required.
The FAA representative leaned back in his chair, and said, “Horse manure explodes in Siberia!”

## Slide 6
Notes: No, not that way.
Apparently, it is so cold in Siberia that manure freezes over. Yet, the inside is still hot, and working. So that, at some point, it breaks through the tough, icy coating and literally explodes.
The point being that unexpected things happen during extreme conditions.
Cav horse

## Slide 7: Why, (Second Senior)
The FAA looks to Canada as experts on cold weather
The Canadian regulations give us the guidance.
Notes: This guy has over 40 years at Cessna and has flown everything from singles to the Citation X
Rick explained that Russia and Canada are considered experts in cold weather testing. The FAA has agreed to follow the Canadian guidelines.

## Slide 8: Why, (Third Senior)
He agrees as to why we test
He also wondered out loud if our survival equipment was “ready”
Notes: This fellow cut his teeth in Vietnam as a helicopter pilot, and has 35 years with Cessna. He, too, has flown all of the Cessna products.
You know, if people would stick to answering only the questions asked, life would be a lot easier.
You see. We have been utilizing the climatic lab so much that we failed to monitor the status of our survival kits and life raft. …
But, I had to follow-up on the equipment readiness.

## Slide 9: What Regulations Apply
According to the cold weather operations section in our FTE Handbook: FAR 25.1301(d), JAR 25.1301(d), AC 25-783-1, and AMA 500C/5B (Transport Canada)
Notes: OK. So, we have the usual catch-all of 1301, an AC, and something called an AMA.
Well, maybe.

## Slide 10: Regulations & ACs
FAR 25.1301(d): Equipment must function properly when installed.
AC 25-783-1: Fuselage Doors, Hatches, and Exits. Replaced by AC 25-783-1 A: Fuselage Doors and Hatches.
AMA 500C/5B is cancelled. Transport Canada now uses the Advisory Circular system. So, AC 500-006 is now applicable.
Notes: As you can see, we no longer have an animal called AMA. Transport Canada has decided to use an AC system.
So, another curious fact is found. One needs to make sure that electronic data bases are maintained.

## Slide 11: Research, AC 500-006
3.0 Background
Past experience has indicated that cold soaked aircraft systems do not always function as predicted. (SIC)Despite cold temperature testing conducted in laboratories on individual components.
The results of a cold soak affect the total aircraft as a system, not just the engine or individual components. The following difficulties could be encountered following a period of aircraft ground cold soak.
Notes: Section 3 points out that individual systems are tested in laboratories. But, the aircraft itself must be considered as one large system--not just the engine, avionics, pressurization, oxygen, etc.

## Slide 12: AC 500-006, 3.0 cont’d
The cold soak test should be of sufficient detail to give reasonable assurance that the aircraft systems will continue to function properly in service and that no potential effect on safety will result from the low temperature soak
Notes: The detail of the testing must ensure proper functionality in service with no effect on safety

## Slide 13: AC 500-006, 4.2 Excerpts
4.2 Test Temperatures
Sections 523.1301-1, 525.1301-1, 527.1301-1 and 529.1301-1 of the AWM require that satisfactory operation of the aircraft be substantiated after exposure, with its engine(s) shut down, to ground ambient temperatures equal to or less than -35ºC unless an alternative minimum ground ambient temperature has been proposed by the applicant and accepted by the Minister
It is recognized that the ground ambient temperature may vary during the soak period and may be warmer than -35ºC at the start of the flight test part of the test and judgment must be used in evaluating the temperature profile against the intent of the requirement (e.g. if the cold soak is carried out overnight based on predicted colder temperatures the following day)
Notes: Canadian Aviation Regulations are broken down into Air Worthiness Manual sub-chapters. Here you see the equivalent to FAR 23, 25, 27 and 29.
The AC gives the guidance on how to apply meaning to cold weather testing and meet the intent of the 1301 requirements.

## Slide 14: AC 500-006, 4.3
4.3 Test Time
The exposure time will vary depending on the type of aircraft and the environment prior to the start of the test. The test should reasonably simulate an overnight cold soak of the aircraft and the exposure time should be at least 10 hours, unless it can be shown that the systems and equipment (including interior) have stabilized at or below the required test temperature
Notes: Obviously, exposure time must have some critical meaning. Here we see the 10 hour requirement commonly noted in test plans.
As you will soon see, we need to know the definition of this "10 hour requirement."

## Slide 15: Typical Overnight Temperature Profile
Notes: As you can see, temperature fluctuates over time. At some point, it wil hit a low point and begin to climb. But, how does it look during winter weather?

## Slide 16: Cold Lake Feb 6, 2007
Notes: This is not an unusually cold temperature for Cold Lake. But, the profile is probably fairly standard. The overnight dip from 1500 hours to 0900 hours before climbing.-- a 19 hour span from hi to lo.

## Slide 17: How to Conduct the Test
Two ways to test
Natural cold weather
Climatic chamber

## Slide 18: Tests in Natural Cold
The safe conduct of tests in natural cold, as compared to a controlled environment, is very similar
So, consider what is not in your control when dealing with Mother Nature

## Slide 19: Wind Chill Factor
Notes: You see it on TV. This is the temp and it feels like ... But, it's more serious than that.
Look at -40. Winds greater than 9 knots push the wind chill effect into the great danger area where flesh may freeze within 30 seconds. Even at -29, with a wind speed greater than 26 knots the risk goes into the great danger area.
Please note the bottom of the chart where the caveat says the individual must be properly clothed.
For you hardy individuals, winds above 35 knots have little change in effect.

## Slide 20: Personal Protective Equipment
Notes: It looks pretty bulky doesn’t it? In the small cockpits it’s nearly impossible to move in and out of the area. So, in the laboratory, we actually remove the seats for test purposes. Something you can’t do in a natural test. Because you must close the doors and takeoff after engine start.
This is the proper way to dress for extreme cold.
lead in to cat

## Slide 22: Test Conduct
Safety Review
Test Plan
Test Card
Monitoring of personnel
Notes: We normally write our test plan for certification directly. However, a development test plan could be required; followed by a certification plan.
A review of the test plans through our Safety Review Board yields our test hazard analysis (THA) which should also cover monitoring of personnel

## Slide 23: Older Test Plan
SAFETY
No unique safety equipment is required for this test.
Risk Assessment: Low
Chase: No
Minimum Crew: No
Telemetry: No
Personal cold weather protection is the safety risk of these tests. A “buddy” system will be used where the test personnel will monitor each others condition to prevent cold weather exposure injury. An appropriate number of survival kits will be carried aboard the aircraft to and from the test site, and all personnel should have appropriate apparel for the cold weather climate.
Notes: This is how we used to cover cold weather safety
Today, we have different processes that you will soon see

## Slide 24: Off Site THA
Notes: Explain the format of the THA
Why two risk factors?

## Slide 25: Test Card
Needs to include all requirements in test plan
Should emphasize the THAs
List the order of things
Be briefed and not strayed from
All personnel involved should be part of the brief (good place to talk about the buddy system)
Notes: Not only are these things written down. We do a dry run prior to departing Wichita. It does not matter if the test is natural or in the lab.

## Slide 26: Monitoring of Personnel
More difficult in natural environment
Usually smaller cadre
Wind chill bigger factor
Covered in our THAs
Notes: Hand-held radios are taken along. Individuals must keep the radios warm for them to work. So, we must be careful not to expose ourselves to the harsh climate.

## Slide 27: Destin, Florida (Eglin AFB)
Notes: What are the advantages of the Climatological Laboratory.

## Slide 28: Chamber Music
Notes: It has a great range of extreme hot to extreme cold as well as, being able to vary other conditions such as wind and icing.

## Slide 29: Briefing Topics – McKinley Laboratory
What does the Lab do?
Lab Services
Admin Topics
Test Hazards
Cold Weather Hazards/ Minimizing Procedures
Hot Weather Hazards/ Minimizing Procedures
Incident Reporting
Notes: McKinley was kind enough to send me their briefing presentation, and I have included the pertinent data in this presentation.

## Slide 30: Briefing Topics (con’t)
Test Conduct
Test Intercom
Test Item Refueling
Fire Suppression Systems
Overtime Support
Environmental Control
Base Services
Summary
Notes: As you can see, most of these items should be covered during natural cold testing, too.

## Slide 31: What does the Lab do?
Mission of the Lab is to support full-scale environmental testing of DOD, non-DOD agencies, and commercial test items
Lab has many unique features such as the world’s largest environmental test chamber and air makeup capabilities to support engine runs
Climatic Lab is staffed by 6 USAF civilians and 40 O&M contractor personnel
Lab supports approximately 20 – 30 tests/ year

## Slide 32: Test Hazards
Tripping hazards
  Cables, tiedowns, etc
  Always look where you’re walking and DON’T
  RUN
Slipping
  Wet/ icy floor
    Wear proper shoes
    Look were you’ re going
  Hydraulic/ oil spills
    Need to be cleaned up ASAP; see TA for
    assistance
Notes: This seems like common sense. However, the worst conditions are during the warm-up when you have a layer of water floating on ice.

## Slide 33: Test Hazards (con’t)
Noise
  Engine operation in chamber
    Wear ear plugs/ crew chiefs need to wear
    noise reducing headsets
Reduced visibility
  Fog in chamber; air makeup run,
  low temps, high humidity
    Situational awareness- know where
    you are and how to get out
Dehydration
  Hot and cold weather
    Drink plenty of fluids
Notes: Air makeup is one area that needs to be coordinated carefully. If the throttle are advanced without warning the vents slam shut and we might get a lot of fog inside the chamber.
Can you find you way out in the fog?

## Slide 34: Cold Weather Hazards
Hypothermia
  Lowering of body heat; symptoms are
  disorientation, loss of memory
Frostbite
  Numbness usually in fingers and toes
Touching metal objects with bare hands
Loose frost accumulation on floor
  Treacherous footing
  Hides electrical and/or instrumentation cables or other tripping hazards
Notes: The buddy system becomes the most powerful prevention of hypothermia and frostbite.

## Slide 35: Minimizing Procedures
Common sense, i.e., if you’re cold, let somebody know
and go warm up!!!
Wear proper clothing and know how it works.
  Always wear gloves.
  Layer clothing.
  Turn in wet gear.
Rotate people out on a regular basis.
Situational awareness-- know what’s around you, and always
know your escape route.
Don’t go in the chamber unaccompanied- use the buddy system.

## Slide 36: Test Conduct
Pre-test briefing before each run to review test cards
TA responsible for overall safety in chamber
TA will announce pending test over PA system
Red flashing light signifying test in progress; non-essential personnel to stay out of chamber
North and south observation rooms available
Minimum number of personnel on floor during testing
Accurate head count of personnel in chamber required
Personnel must clear with TA on entering and exiting the chamber
Notes: Test Advisor
Also a Test Conducter

## Slide 37: Test Conduct (con’t)
Fire exits should be discussed in pre-test briefings.
In the event of an evacuation, all personnel should exit
the chamber, and meet in the Test Assembly building for
a head count.
Fire truck standing by outside V-door, fire guard in TA
Booth.
Exhaust door monitor.
Pilot must clear any APU and engine operation change
with the Lab air-makeup operator.
Any problems can be addressed in de-briefs.

## Slide 38: Test Conduct (con’t)
EMERGENCY CALLS during engine operation
  “COME TO IDLE” means a problem has been noticed, which requires a reduction in engine power. Pilot will bring the engine to idle; person who made the call will then report.
  “ABORT, ABORT” means a problem has been noticed requiring immediate engine shutdown. Pilot will shutdown the engine; person who made the call will then report.
Emergency calls should be reviewed during pre-run briefings.

## Slide 40: Laboratory THA

## Slide 41: Setup and Testing
Set aircraft on stands
Align exhaust chutes
Restrain with chains
Begin cooling by Noon
-20 degrees C by 2200
-40 degrees C by 0400 the next day
Can easily begin testing by 0800?
Notes: This would be a typical setup and cool down profile

## Slide 42: But wait/ There’s More
The AC has a section addressing the AFM
It suggests the way to determine Cold Weather Limitations

## Slide 43: AC 500-006, Section 5
Where cold soak test temperature of -35ºC has not been achieved (a) A statement in the Limitations Section that operation is prohibited if the aircraft, with its engine(s) shut down is exposed to a ground ambient temperature below a stated temperature, which is the actual minimum cold soak temperature achieved (e.g. engine start below an ambient temperature of –20oC is prohibited)

## Slide 44: AC 500-006, Section 5
This limitation is used where a prolonged cold soak has been demonstrated to an average temperature higher than -35ºC and no demonstration has been conducted to identify aircraft performance following a brief exposure (less than 10 hours) to a temperature lower than -35ºC

## Slide 45
Notes: Here's something you can't do in the natural environment. If you power up on an icy surface you can't control the aircraft very well. In the chamber we can power up, and even function gear and flaps if restrained properly.

## Slide 46
Notes: Here's a gee whiz example of what might occur during an engine start in extreme cold.
What happened to ABORT ABORT?
The response of the Test Conductor was too cavalier. He should have yelled a very strong ABORT, ABORT ABORT.

## Slide 47
Notes: Changing the test procedure on-the-fly

## Slide 48: SUMMARY
Just like any other task requiring two or more people
working together, communication is the key to success
A dry run prior to departing for cold weather gives individual personnel the chance to see what to expect prior to facing the cold. It also gives the opportunity to improve your test plan prior to departing home if need be
If you want a “sure thing” go to the Lab.- don’t chase weather
Notes: O, before I go. Some people feel that global warming will negate the need for cold weather testing. Even if it does, it won't be in our life times.
However, I do have some proof of this phenomena over time.